## Slide 1
Full System Integration
Arduino · HiveMQ · Node.js · Browser
Architecture · Checks · Interface Checks · Data Flow
1. Architecture
2. Within-Step Checks
3. Cross-Step Checks
4. Data Payloads
ArduinoMqttClient · mqtt.js · Socket.io · HiveMQ Cloud EU · Open-Meteo

## Slide 2
Full System Map
All components · all protocols · all data flows
Browser
index.html
Socket.io client
Node.js Server
Express · Socket.io
mqtt.js · dotenv
HiveMQ Cloud
MQTT Broker
port 8883 / TLS
Arduino
ESP32-S3
FreeRTOS 9 tasks
ArduinoMqttClient
Open-Meteo API
free, no API key
fetch() 10min
WebSocket
MQTT/TLS
MQTT/TLS
Socket.io client
Device dropdown
Login form
Range validation
boilerStates cache
authorized room
weather timer
stale watchdog
Topic routing
Retained msgs
LWT delivery
TLS auth
9 FreeRTOS tasks
JSON telemetry
NTP + TLS
systemHealth WDT

## Slide 3
Phase 1 — Initialization & Connection
Arduino boot · WiFi · NTP · TLS · MQTT · Node.js startup
ARDUINO (TaskCloud)
FreeRTOS boots → 9 tasks created, TaskCloud at priority 2
WiFi: try SSID1 (Sunrise_2.4GHz) — if no connect in 10 s, fallback SSID2 (OnePlus)
NTP: configTime(pool.ntp.org) → poll time() every 500 ms, up to 40 retries (20 s max)
TLS: setCACert(ROOT_CA) → connect to HiveMQ:8883 via mbedTLS
MQTT: register LWT 'offline' on boilers/ESP/status (retained)
Success: publish 'online' → subscribe commands + weather topics
NODE.JS SERVER STARTUP
dotenv.config() → loads MQTT/WEB credentials from .env file
mqtt.connect() with clientId 'Server_Bridge_Main', clean:true, reconnect 1s
on('connect'): subscribe boilers/# → fetchWeatherData() → start 10-min timer
CHECKS IN THIS PHASE
✓
WiFi: dual SSID fallback, infinite retry loop
✓
NTP: wait up to 20 s — required before TLS handshake
✓
TLS: mbedTLS verifies ROOT_CA (Let's Encrypt YR2 cert)
✓
MQTT: up to 5 connect retries before TaskCloud exits
✓
Node.js .env: missing creds → MQTT auth error on connect
✓
weatherInterval guard prevents duplicate timers on reconnect
Critical interface check — NTP → TLS dependency: ROOT_CA is valid from Sep 2025. If time() < 1700000000 at TLS handshake, mbedTLS returns -9984. NTP sync is a hard prerequisite for MQTT.

## Slide 4
Phase 2 — Browser Loads & Connects
HTTP page load · Socket.io connect · immediate state delivery from cache
ARCHITECTURE
Browser HTTP GET / → Express serves /public/index.html + static assets
Socket.io client loaded → ws:// connect to Node.js server
Node.js fires io.on('connection') → immediately iterates boilerStates{}
Emits 'boilerUpdate' for each cached device — browser sees last known values instantly
Emits 'bridgeStatus': connected/disconnected based on MQTT client state
WHAT BROWSER SHOWS IMMEDIATELY
If boilerStates has data → last known sensor values shown, no wait needed
If boilerStates is empty → blank UI, waits for next Arduino telemetry cycle
bridgeStatus 'disconnected' → red 'Bridge offline' banner shown
Auth NOT required to receive data — controls stay hidden until login
CHECKS IN THIS PHASE
✓
No auth needed to connect — telemetry open to all sockets
✓
client.connected checked before sending bridgeStatus
✓
Object.values(boilerStates) iterates all known devices
✗
Cached state may be stale — no freshness check at connect
CROSS-STEP INTERFACE CHECKS
Browser ↔ Node.js: socket open — login only unlocks controls
Node.js ↔ HiveMQ: connected at Phase 1 — page load does not re-trigger
HiveMQ: Arduino 'online' retained in broker — no extra subscribe
HiveMQ offline → bridgeStatus 'disconnected' sent to new browser

## Slide 5
Telemetry Data Flow — Arduino to Browser
Every 15 s: sensor JSON travels from boiler to every open browser tab
Arduino
ESP32-S3
HiveMQ
Cloud
Node.js
mqtt.js
boilerStates
cache
Browser(s)
Socket.io
boilers/ESP/status retain:true
{ "deviceId":"ESP",
"dhtTempC":15.2, "homeTempC":18.5,
"heaterWaterTemp":55.2,
"heaterState":true,
"targetHomeTemp":20.0,
"systemHealth":63 }
Node.js merges into boilerStates[deviceId]
adds lastSeen:Date.now(), connectionStatus:'online'
io.emit('boilerUpdate')
io.emit('boilerStatusUpdate')
CHECKS AT EACH HOP
JSON built every 15 s via vTaskDelayUntil
retain:true — new subscriber gets it immediately
Fields from FreeRTOS global variables
Routes to all boilers/# subscribers
Retained copy stored per topic
LWT 'offline' replaces on disconnect
JSON.parse in try/catch — bad JSON logged
topicParts[1] extracts deviceId
lastSeen update resets stale watchdog
Spread merges fields over existing cache
Last values kept if field missing
Available instantly for new browsers
All open tabs update simultaneously
Dropdown selects which device to show
No persistence — all from socket push

## Slide 6
Command Data Flow — Browser to Arduino
User controls travel through auth gate, MQTT, and land on the actuators
User
UI Control
Node.js
Auth Gate
HiveMQ
Cloud
Arduino
callback
Actuators
Applied
not authorized
→ silent drop
emit('heaterCommand')
{ "deviceId":"ESP",
"payload": {
"command":"setTargetTemp",
"targetTemp":22.0,
"boilerSetpoint":65.0 } }
client.publish('boilers/ESP/commands', payload)
qos:0, retain:false — only live Arduino receives it
onMqttMessageReceived
→ JSON.parse → clamp → apply
CHECKS AT EACH HOP
Temp range: 5–30 °C
Setpoint range: 40–70 °C
Controls hidden until login success
socket.rooms.has('authorized')
Silent drop if not authorized
No rate limiting server-side
Routes to all commands subscribers
Not retained — stale not replayed
Dropped if Arduino offline
ArduinoJson parses command
Safety clamping before globals
sendHeaterData() called immediately
Relay or valve position updated
FreeRTOS notifications trigger tasks
WDT requires systemHealth=0x3F

## Slide 7
Weather Data Flow — API to Arduino
Open-Meteo outdoor temperature injected via MQTT every 10 minutes
Open-Meteo
REST API
Node.js
fetch()
HiveMQ
retain:true
Arduino
MQTT sub
DHT Task
override
GET /v1/forecast?lat=46.52769&lon=7.06050
&current=temperature_2m,relative_humidity_2m
boilers/B1/weather + boilers/ESP/weather
{ "command":"weather",
"outdoorTemp":8.5, "outdoorHumidity":78 }
Arduino receives:
g_outdoorTempC = json["outdoorTemp"]
g_outdoorHumidity = json["outdoorHumidity"]
g_useCloudWeather = true
TaskDHT: if g_useCloudWeather skip
physical sensor read — use cloud values
CHECKS AT EACH HOP
Free REST API, no auth key
try/catch on fetch failure — logs error, skips publish
Returns JSON with current{} block
weatherInterval guard — no duplicate timers
Published to both device topics
retain:true — Arduino gets it on subscribe
Retained stored per topic
Delivered immediately on subscribe
Overwritten every 10-min cycle
Parsed in onMqttMessageReceived
g_useCloudWeather persists until reboot
TaskDHT flag checked each loop cycle
WaterActuator uses outdoorTempC
HomeTempModel heat loss uses it
More accurate than sensor board temp

## Slide 8
Checks Within Each Component
What each component validates internally before acting
Arduino
✓
WiFi: dual SSID fallback, retry loop
✓
NTP: wait 20 s before TLS connect
✓
TLS: ROOT_CA cert via mbedTLS
✓
MQTT: 5 connect retries max
✓
Commands: value clamping applied
✓
systemHealth WDT: all 6 bits required
✗
No NTP → TLS fails (-9984)
✗
MQTT fail → systemHealth bit stays 0
HiveMQ Cloud
✓
TLS handshake required
✓
Username + password auth
✓
Retained msgs per topic
✓
LWT delivery on unclean disconnect
✓
Wildcard boilers/# routing
✗
Bad credentials → refused
✗
No matching subscriber → dropped
✗
Offline publisher → LWT sent
Node.js
✓
Auth gate: rooms.has('authorized')
✓
JSON parse: try/catch in handler
✓
weatherInterval stacking guard
✓
Stale watchdog: 30 s / 90 s
✓
client.connected before emit
✗
Bad JSON → logged, ignored
✗
Unauthorized command → dropped
✗
HiveMQ down → reconnect loop
Browser
✓
Temp range 5–30 °C before emit
✓
Setpoint range 40–70 °C
✓
switchDevice: checks cache exists
✓
Controls hidden until login
✓
Status banners reflect all errors
✗
Out-of-range blocked before emit
✗
No login → commands gate at Node.js
✗
Bridge offline → red banner shown

## Slide 9
Interface Checks Between Components
What is verified at each connection boundary
Browser ↔ Node.js (WebSocket / Socket.io)
✓
B→N
No auth to connect or receive telemetry — data open to all sockets
✓
B→N
'login' event: creds compared against WEB_USERNAME + WEB_PASSWORD from .env
✓
B→N
'heaterCommand' processed only if socket.rooms.has('authorized') is true
✗
N→B
Socket disconnect → room membership lost — user must log in again
Node.js ↔ HiveMQ (MQTT / TLS port 8883)
✓
N→H
MQTTS protocol — TLS required, no plaintext fallback possible
✓
N→H
Username + password from .env — wrong creds → connection refused
✓
N→H
clientId 'Server_Bridge_Main' fixed, clean:true — no stale session
✗
H→N
HiveMQ unreachable → reconnectPeriod 1000 ms loop, 'reconnecting' status to browsers
HiveMQ ↔ Arduino (MQTT / TLS port 8883)
✓
A→H
TLS: ROOT_CA (Let's Encrypt YR2) verified by mbedTLS — requires valid NTP clock
✓
A→H
LWT registered at connect: topic=boilers/ESP/status, msg='offline', retain:true
✓
H→A
Retained weather + old telemetry delivered immediately on Arduino subscribe
✗
A→H
Cert expiry (~Sep 2028): run openssl s_client -connect <host>:8883 -showcerts to get new cert

## Slide 10
Error States & Recovery
What breaks, what the system does, and how the UI reflects each failure
Arduino disconnects (unclean)
1
Arduino: WiFi drops or MQTT crashes (no clean disconnect)
2
HiveMQ detects TCP timeout → delivers stored LWT message
3
LWT: 'offline' published to boilers/ESP/status (retained)
4
Node.js on('message') sets connectionStatus='offline' in cache
5
Node.js io.emit('boilerStatusUpdate', {status:'offline'})
6
Browser: red device-offline banner shown immediately
LWT delivery is instant — no 90-second wait
Arduino freezes silently (no LWT)
1
Arduino: FreeRTOS task hangs, TCP stays open — no LWT
2
HiveMQ: connection appears live — no LWT triggered
3
Node.js stale watchdog: setInterval 30 s checks lastSeen
4
After 90 s silence: state.connectionStatus = 'no-data'
5
io.emit('boilerStatusUpdate', {status:'no-data'})
6
Browser: orange no-data banner shown
Only mechanism to catch a silent freeze
Node.js loses HiveMQ connection
1
mqtt.js fires on('offline')
2
io.emit('bridgeStatus', {status:'disconnected'}) to all tabs
3
Browser shows red 'Bridge disconnected' banner instantly
4
mqtt.js auto-reconnect loop every 1000 ms
5
on('reconnect'): bridgeStatus 'reconnecting' emitted
6
On success: re-subscribe boilers/# + re-fetch weather
boilerStates cache preserved during outage
Arduino WDT reset (systemHealth)
1
9 FreeRTOS tasks each set a bit in systemHealth
2
TaskWatchdog: if systemHealth != 0x3F → WDT not kicked
3
Hardware WDT fires after 3 s of no kick → board resets
4
Full Phase 1 init restarts (WiFi + NTP + TLS + MQTT)
5
LWT 'offline' delivered by HiveMQ during reset gap
6
On reconnect: 'online' published + telemetry resumes
Bits: 0=HomeTemp 1=HeaterTemp 2=DHT 3=WaterAct 4=Heater 5=Cloud

## Slide 11
JSON Payload Reference
All message formats used — every MQTT topic and Socket.io event
Telemetry — boilers/ESP/status
retain:true qos:0
{
"deviceId": "ESP",
"dhtTempC": 15.2,
"dhtHumidity": 62.0,
"homeTempC": 18.5,
"heaterWaterTemp": 55.2,
"heaterActivation": 1,
"heaterState": true,
"waterpumpactivation": 1,
"waterValvePosition": 0.65,
"targetHomeTemp": 20.0,
"systemHealth": 63
}
63 = 0x3F = all 6 task bits set
Command — boilers/ESP/commands
retain:false qos:0
{
"command": "setTargetTemp",
"targetTemp": 22.0,
"boilerSetpoint": 65.0
}
// Or heater on/off:
{
"command": "setHeaterState",
"heaterState": true
}
Non-retained — stale not replayed on reconnect
Weather — boilers/B1+ESP/weather
retain:true qos:0
{
"command": "weather",
"outdoorTemp": 8.5,
"outdoorHumidity": 78
}
// Source:
// api.open-meteo.com/v1/forecast
// lat=46.52769 lon=7.06050
Retained — Arduino receives on subscribe

## Slide 12
Integration Summary
Each component has a distinct role — together they form a resilient real-time IoT bridge
Arduino ESP32-S3
Sensor reader + actuator driver
9 FreeRTOS tasks, priority-scheduled
NTP sync → TLS connect → LWT register
JSON publisher every 15 s (retain:true)
Receives commands + weather via MQTT
systemHealth WDT safeguards hardware
HiveMQ Cloud
Pure MQTT broker — no app logic
Routes messages publisher → subscriber
Retained msgs: instant state on subscribe
LWT: auto-offline on unclean disconnect
TLS auth gate at port 8883
Wildcard topics enable multi-device
Node.js Bridge
Bridges MQTT ↔ WebSocket
boilerStates cache for new connections
authorized room gates commands
Weather fetcher every 10 minutes
Stale watchdog: 90 s timeout
Auto-reconnects to HiveMQ and browsers
Browser (index.html)
Single HTML file, zero build step
Device dropdown — multi-board UI
Login → Socket.io room → commands unlock
Client-side range validation before emit
Status banners reflect all error states
All data via Node.js push — no polling