## Slide 1: HiveMQ Cloud
Arduino Uno R4 Wifi

## Slide 2: Goal: Establish a stable, zero-cost bridge between the Arduino R4 and your Node.js server.
Protocol: MQTT (Message Queuing Telemetry Transport).
Platform: HiveMQ Cloud (Free Tier - up to 100 devices).
Security: TLS encryption (Port 8883) using Username/Password instead of complex X.509 certificates.
Benefit: Zero-footprint on R4 memory, faster handshake, and no monthly billing.

## Slide 3: The "Envelope" Method: Instead of 20 separate messages, we will use JSON.
Payload: A single JSON object containing all 20 variables.
Topic Structure: boiler/main/status
Example Payload: {"temp": 72.5, "pressure": 1.2, "relay": true, "target": 75.0, ...}
Efficiency: Reduces WiFi "on-time" and prevents the Arduino from hanging during transmission.

## Slide 4: Responsibility: Data collection and transmission.
Read: Sample 20 sensors/variables every 30 seconds.
Pack: Use the ArduinoJson library to build the "Envelope."
Ship: Connect via WiFiS3 and ArduinoMqttClient to HiveMQ.
Safety: If the connection fails, the Arduino continues its local heater safety logic independently (Asynchronous).

## Slide 5: Responsibility: Data processing and distribution.
Listen: Stay permanently connected to HiveMQ via the mqtt npm package.
Unpack: Receive the JSON string and parse it back into a JavaScript object.
Broadcast: Use Socket.io to "push" the fresh data to every connected HTML dashboard instantly.
Log: (Optional) Save the data to a local file or database for history

## Slide 6: Responsibility: Real-time visualization.
Socket Connection: Open a "hotline" to your local Node.js server.
Dynamic Update: When a message arrives, update the UI (gauges, charts, or text) without refreshing.
User Input: Send "Target Temp" changes back up the chain (HTML $\rightarrow$ Node.js $\rightarrow$ HiveMQ $\rightarrow$ Arduino).

## Slide 7
The Master Roadmap: From Arduino to Desktop App
Phase 1: The Cloud "Switchboard" (HiveMQ)
  Step 1: Create the HiveMQ Free Cluster.
  Step 2: Define the Multi-Boiler Topic Structure: boilers/{{DEVICE_ID}}/status.
  Step 3: Generate secure credentials for the hardware and the server.
Phase 2: The Hardware "Pulse" (Arduino R4)
  Step 4: Define a unique DEVICE_ID for each R4 (e.g., B1, B2).
  Step 5: Implement JSON Bundling: Pack all 20 variables into one message.
  Step 6: Asynchronous Publishing: Send data every 30 seconds without blocking the heater logic.
Phase 3: The Local "Brain" (Node.js)
  Step 7: The Wildcard Listener: Set up Node.js to listen to boilers/+/status so it catches data from all connected boilers.
  Step 8: Data Logging (Hard Drive): Implement a local storage system (JSON or SQLite) to save every data point permanently to your laptop.
  Step 9: Socket.io Bridge: Stream the live data from Node.js to your HTML dashboard.
Phase 4: The Final Product (The .exe Dashboard)
  Step 10: Build the Multi-Card UI: Design the dashboard to show a new status card automatically whenever a new Boiler ID appears.
  Step 11: Electron Packaging: Wrap the Node.js server and HTML into a portable .exe file.
  Step 12: Distribution: Test the .exe on a different computer/network to confirm it sees the boiler.

## Slide 8: Setting up HiveQM
Create a serverless cluster
d72dc8b632b04c8c91c4702a5b164d59.s1.eu.hivemq.cloud: this is my link
1. The Standard URL & Port (8883)
What it is: The "Professional Entrance."
Who uses it: Your Arduino R4.
Why: Port 8883 is the industry standard for Secure MQTT. It uses TLS (Transport Layer Security), which is the same encryption banks use. Since your Arduino is a dedicated hardware device, it speaks the "pure" MQTT language directly.
2. WebSocket Port (8884)
What it is: The "Web Entrance."
Who uses it: Your Browser / Dashboard.
Why: Standard browsers (like Chrome or Safari) are "allergic" to pure MQTT; they only like to speak Web languages. The WebSocket port wraps the MQTT data inside a web-friendly package. You’ll use this when you want your HTML page to show live data without going through a server.
3. TLS MQTT URL
What it is: Just a combined version of #1.
Note: It’s exactly the same as the first URL, just with :8883 added to the end. Most code libraries ask for the "Host" and the "Port" separately, but some want the whole string.
4. TLS WebSocket URL
What it is: The full address for web-based tools.
Note: Notice the /mqtt at the end. This is the specific "path" a website follows to find the data stream.