## Slide 1
ESP32-S3 Heater Project
Source Code Reference — Function by Function
9
Source Files
24
Functions
9
FreeRTOS Tasks
PlatformIO · FreeRTOS · MQTT / TLS · HiveMQ Cloud

## Slide 2
SOURCE FILE
main.cpp
System entry point, shared globals, hardware initialisation, task registry, and hardware WDT monitor task.

## Slide 3
setup()
main.cpp
PURPOSE
System boot sequence. Initialises all hardware peripherals: DHT11, heater relay, H-bridge motor driver (IN1/IN2/ENABLE), and servo. Creates all 9 FreeRTOS tasks in a deliberate order and starts the hardware watchdog.
KEY POINTS
TaskCloud created first — priority 2, 8192-word stack for TLS
All other tasks at priority 1, 2048-word stack each
Watchdog: esp_task_wdt_init(5, true) — resets on fire
ESP32 FreeRTOS auto-starts — no vTaskStartScheduler() call needed
100ms delay after servo attach for MCU stabilisation

## Slide 4
loop()
main.cpp
PURPOSE
Intentionally empty. The FreeRTOS scheduler takes full control after setup() completes. All real work runs inside the 9 FreeRTOS tasks, each with its own stack and driven purely by notifications from the scheduler.
KEY POINTS
Left empty by design
Arduino's loop() runs in a low-priority ESP-IDF task
FreeRTOS scheduler pre-empts it immediately
No polling, no busy-waiting — all work is event-driven

## Slide 5
TaskwatchdogMonitor()
main.cpp
PURPOSE
Final system health guardian. Wakes once per cycle (slot 8, notified by the scheduler). Checks that all 6 worker tasks have set their health bits in systemHealth, then decides whether to kick the hardware WDT or let it fire.
KEY POINTS
Registers itself with WDT via esp_task_wdt_add(NULL)
Blocks on ulTaskNotifyTake(portMAX_DELAY)
Checks systemHealth == HEALTH_REQUIRED (0x3F)
Kicks WDT via esp_task_wdt_reset() only if all 6 bits set
Resets systemHealth to 0x00 every cycle regardless of outcome

## Slide 6
SOURCE FILE
Scheduler.cpp
Master heartbeat task. Runs at priority 3 and drives all other tasks at a precise 250 ms cadence using vTaskDelayUntil().

## Slide 7
TaskTimeScheduler()
Scheduler.cpp
PURPOSE
Master timing heartbeat. Runs at priority 3 — the highest in the system. Notifies every task in sequence with a 250 ms gap between slots using xTaskNotifyGive(). Cloud telemetry is rate-limited independently to every 15 seconds.
KEY POINTS
Priority 3 — no worker task can preempt it
8 task slots × 250 ms = 2-second full round
vTaskDelayUntil() absorbs notification overhead — no timing drift
Cloud notified only when 15s have elapsed since last send
Null-checks each task handle before notifying (safe startup)

## Slide 8
SOURCE FILE
DataToCloud.cpp
Full WiFi / MQTT cloud lifecycle: connection, telemetry publish, command reception, and 10-minute offline watchdog.

## Slide 9
TaskCloud()
DataToCloud.cpp
PURPOSE
MQTT connection lifecycle manager. Uses a 500 ms timed notification wait as a dual-purpose mechanism: poll the MQTT client for keepalive every 500 ms, and react immediately when the scheduler triggers a telemetry publish (every 15 s).
KEY POINTS
ulTaskNotifyTake with 500ms timeout (poll + notify in one call)
Tracks lastConnectionTime while connected
10-minute offline countdown → esp_restart() for recovery
Calls sendHeaterData() only when mqttClient.connected()
isDegradedMode flag signals UI of degraded connectivity

## Slide 10
initializeCloud()
DataToCloud.cpp
PURPOSE
Full startup connection sequence. Connects to WiFi (with automatic SSID2 fallback on timeout), verifies IP assignment, syncs NTP, configures MQTT credentials and Last Will & Testament, sets the TLS CA certificate, and connects to HiveMQ with up to 10 retry attempts.
KEY POINTS
SSID1 → 5s timeout → automatic SSID2 fallback
LWT: broker publishes 'offline' on unexpected disconnect
wifiClient.setCACert(ROOT_CA) — ESP32 has no built-in CA store
WDT kicked at 3 blocking points (WiFi done, before TLS, after connect)
Subscribes to commands + weather topics on success

## Slide 11
sendHeaterData()
DataToCloud.cpp
PURPOSE
Serialises the complete system state into a JSON payload and publishes it to boilers/ESP/status as a retained MQTT message. Called every 15 seconds by the scheduler notification, and also immediately after any command is received.
KEY POINTS
14-field JSON: pump, boiler temp, home temp, DHT, valve, health...
Retained message — UI receives latest state on connect, before next publish
Payload serialised to String first — avoids ArduinoMqttClient 256-byte limit
Called on schedule AND after every command for immediate UI feedback

## Slide 12
onMqttMessageReceived()
DataToCloud.cpp
PURPOSE
MQTT message callback registered with mqttClient.onMessage(). Parses incoming JSON from the commands topic and routes each command to the correct global variable. Safety clamping is applied on the Arduino side regardless of what the server sends.
KEY POINTS
"heater" → heaterState (only when manualOverride is active)
"temperature" → targetHomeTemp, clamped 5–30 °C
"manualOverride" → switches between auto and manual mode
"heaterSetPoint" → heaterTempSetPoint, clamped 40–70 °C
"weather" → outdoor data from Open-Meteo, sets g_useCloudWeather

## Slide 13
SOURCE FILE
Heater.cpp
Heater relay control and automatic thermostat logic with 5 °C hysteresis to prevent rapid relay cycling.

## Slide 14
TaskHeater()
Heater.cpp
PURPOSE
FreeRTOS task wrapper. Blocks indefinitely on ulTaskNotifyTake() until the scheduler sends a notification (slot 1 — the first task woken each 250 ms cycle). Immediately dispatches to doHeaterSequence().
KEY POINTS
First task notified every cycle (slot 1 of 8)
Blocks with portMAX_DELAY — zero CPU use while idle
Priority 1, 2048-word stack
No logic here — pure notification-to-action dispatch

## Slide 15
doHeaterSequence()
Heater.cpp
PURPOSE
Drives the physical heater relay to match heaterState. When manual override is disabled, automatically recalculates heaterState from boiler water temperature vs. setpoint with a 5 °C hysteresis band to prevent rapid relay cycling.
KEY POINTS
Relay: digitalWrite(HIGH) if heaterState, LOW otherwise
Auto mode (manualOverride == false):
ON when g_heaterWaterTemp < heaterTempSetPoint
OFF when g_heaterWaterTemp > setPoint + 5 °C
Sets systemHealth |= (1 << 4)

## Slide 16
SOURCE FILE
WaterActuator.cpp
Water pump and servo valve control. 3-zone proportional logic with hysteresis and analytical equilibrium valve calculation.

## Slide 17
TaskWaterActuator()
WaterActuator.cpp
PURPOSE
FreeRTOS task wrapper. Wakes on notification from the scheduler (slot 2, 250 ms after TaskHeater), then calls doWaterActuatorSequence(). Blocks indefinitely between wakeups.
KEY POINTS
Slot 2 in the scheduler — wakes 250 ms after TaskHeater
Blocks on ulTaskNotifyTake(portMAX_DELAY)
Priority 1, 2048-word stack
Dispatches to doWaterActuatorSequence()

## Slide 18
driveWaterPump()
WaterActuator.cpp
PURPOSE
Controls the H-bridge motor driver (in1Pin, in2Pin, enablePin) to run or stop the water circulation pump. Updates g_WaterPumpSpeed and sets health bit 0 to signal the watchdog.
KEY POINTS
spd > 0: IN1=HIGH, IN2=LOW, analogWrite(enable, 255)
spd == 0: IN1=LOW, IN2=LOW, analogWrite(enable, 0)
g_WaterPumpSpeed set to 100 (running) or 0 (stopped)
Sets systemHealth |= (1 << 0) — pump health bit

## Slide 19
controlHomeTemp()
WaterActuator.cpp
PURPOSE
3-zone thermostat selecting pump speed and valve angle based on home temperature vs. target. Uses ±0.5 °C deadband and 0.2 °C hysteresis to prevent rapid zone switching at boundaries.
KEY POINTS
Zone 1 (cold): pump ON, valve 180° — maximum heat delivery
Zone 2 (equilibrium): pump ON, valve at analytically computed angle
Zone 3 (warm): pump OFF, valve 0° — no heat delivery
Equilibrium: solve gainFactor so heat gain exactly equals heat loss
Hysteresis: must cross 0.2 °C past boundary before changing zone

## Slide 20
doWaterActuatorSequence()
WaterActuator.cpp
PURPOSE
Thin wrapper called each cycle by TaskWaterActuator. Runs the full 3-zone control logic and then sets the valve health bit in the system health bitmask.
KEY POINTS
Calls controlHomeTemp() to apply 3-zone logic
Sets systemHealth |= (1 << 5) — valve health bit
Health bits 0 (pump) and 5 (valve) are both required
Watchdog considers this task healthy only when both bits are set

## Slide 21
SOURCE FILE
Sensors.cpp
Three FreeRTOS tasks: home air temperature model, boiler water temperature model, and physical DHT11 sensor read.

## Slide 22
TaskHomeTemp()
Sensors.cpp
PURPOSE
FreeRTOS task wrapper for the home air temperature simulation. Wakes on notification from the scheduler (slot 4) and calls doHomeTempRead() to advance the HomeTempModel by one time step.
KEY POINTS
Slot 4 in the scheduler — wakes 750 ms into each cycle
Blocks on ulTaskNotifyTake(portMAX_DELAY)
Priority 1, 2048-word stack
Delegates all logic to doHomeTempRead()

## Slide 23
TaskHeaterTemp()
Sensors.cpp
PURPOSE
FreeRTOS task wrapper for the boiler water temperature simulation. Wakes on notification (slot 3) and calls doHeaterTempRead() to advance the HeaterModel by one time step.
KEY POINTS
Slot 3 in the scheduler — wakes 500 ms into each cycle
Blocks on ulTaskNotifyTake(portMAX_DELAY)
Priority 1, 2048-word stack
Delegates all logic to doHeaterTempRead()

## Slide 24
TaskDHT()
Sensors.cpp
PURPOSE
FreeRTOS task wrapper for the physical DHT11 sensor. Wakes on notification (slot 5) and calls doDHTRead() to perform the humidity and temperature read from the sensor.
KEY POINTS
Slot 5 in the scheduler — wakes 1000 ms into each cycle
Blocks on ulTaskNotifyTake(portMAX_DELAY)
Priority 1, 2048-word stack
Delegates all logic to doDHTRead()

## Slide 25
doHomeTempRead()
Sensors.cpp
PURPOSE
Advances the home air temperature simulation by one real-time step and signals the watchdog. Delegates the physics calculation entirely to updateHomeTempModel() in HomeTempModel.cpp.
KEY POINTS
Calls updateHomeTempModel() — defined in HomeTempModel.cpp
Sets systemHealth |= (1 << 1)
Health bit 1 = home temperature model ran this cycle

## Slide 26
doHeaterTempRead()
Sensors.cpp
PURPOSE
Advances the boiler water temperature simulation by one real-time step and signals the watchdog. Delegates the physics calculation to updateHeaterModel() in HeaterModel.cpp.
KEY POINTS
Calls updateHeaterModel() — defined in HeaterModel.cpp
Sets systemHealth |= (1 << 2)
Health bit 2 = heater temperature model ran this cycle

## Slide 27
doDHTRead()
Sensors.cpp
PURPOSE
Reads temperature and humidity from the physical DHT11 sensor. Skips the hardware read entirely when cloud weather is active, so real outdoor data from Open-Meteo (pushed via MQTT) is not overwritten by the indoor sensor.
KEY POINTS
If g_useCloudWeather == true: sets health bit and returns immediately
Reads dht.readHumidity() and dht.readTemperature()
NaN on sensor error → sentinel values 100 / 100 written to globals
Sets systemHealth |= (1 << 3)

## Slide 28
SOURCE FILE
HeaterModel.cpp
Boiler water temperature simulation (to be replaced by a real sensor). Heater ON rises linearly; OFF cools with outdoor-dependent rate.

## Slide 29
updateHeaterModel()
HeaterModel.cpp
PURPOSE
Simulates g_heaterWaterTemp over time based on heater relay state and outdoor temperature. Called every 250 ms. Computes a real elapsed-time delta (millis) for physics accuracy.
KEY POINTS
First call: timer init only — no temperature change
Heater ON: +1 °C per 20 s, hard cap at 90 °C
Heater OFF: cooling rate interpolated by outdoor temperature
−5 °C outdoor → 1 °C per 10 min (fastest cooling)
+30 °C outdoor → 1 °C per 20 min (slowest cooling)

## Slide 30
SOURCE FILE
HomeTempModel.cpp
Home air temperature simulation using Newton's law of cooling with boiler heat gain and bidirectional outdoor heat exchange.

## Slide 31
updateHomeTempModel()
HomeTempModel.cpp
PURPOSE
Simulates g_homeTemp over time. Applies two simultaneous heat exchange processes each step: heat gain from the boiler (valve and pump-dependent) and bidirectional thermal exchange with the outdoor environment.
KEY POINTS
First call: timer init only — no temperature change
Heat gain (pump running only): HEAT_GAIN_RATE × gainFactor × ΔT_boiler × Δt
gainFactor: 10% at valve 0°, 100% at valve 180°
Outdoor exchange: HEAT_LOSS_RATE × (home − outdoor) × Δt (bidirectional)
~24h to equilibrate with outdoors; ~15min to reach boiler temp (full open)

## Slide 32
SOURCE FILE
HeapMonitor.cpp
FreeRTOS runtime diagnostics: stack high-water marks for all 9 tasks, free heap, minimum-ever heap, and health bitmask.

## Slide 33
TaskMonitor()
HeapMonitor.cpp
PURPOSE
FreeRTOS diagnostic task. Wakes once per cycle when notified by the scheduler (slot 7) and calls printRtosStats() to dump a full diagnostics block to the serial console.
KEY POINTS
Slot 7 in the scheduler — wakes 1500 ms into each cycle
Blocks on ulTaskNotifyTake(portMAX_DELAY)
Priority 1, 2048-word stack
Delegates output to printRtosStats()

## Slide 34
printRtosStats()
HeapMonitor.cpp
PURPOSE
Prints a complete diagnostics block to serial: stack high-water mark for every task, current free heap, minimum-ever free heap, and the systemHealth bitmask in binary. All output is guarded by the DEBUG macro and compiles out completely in production.
KEY POINTS
All output via D_PRINT/D_PRINTLN — zero overhead in production
Stack HWM = minimum free words ever seen → detects overflow risk
MinEver heap: tracks memory fragmentation over long uptime
systemHealth printed in binary — each bit maps to one task
Covers all 9 tasks: Heater, WaterAct, Temps, DHT, Heap, Sched, WDT, Cloud